## Slide 1: Lecture 15: IP addressing
(Revisited)

## Slide 2: Octets
The 32-bit IP address is broken up into 4 octets, which are arranged into a dotted-decimal notation scheme.
An octet is a set of 8 bits & not a musical instrument.
Example of an IP version 4:
172.64.126.52

## Slide 3: Converting to Decimal
You’ll need to convert binary to decimal & vice versa to compute subnets & hosts.
So, it’s time for a quick review lesson in binary-to-decimal conversion.
There are 8 bits in an octet & each bit can only be a 1 or a 0.

## Slide 4: Converting to Decimal (Cont.)
What then do you suppose is the largest decimal number that can be expressed in an octet?
Eight 1’s (1111 1111)

## Slide 5: IP Address Classes
IP addresses are divided into 5 classes, each of which is designated with the alphabetic letters A to E.
Class D addresses are used for multicasting.
Class E addresses are reserved for testing & future use.

## Slide 6: IP Address Classes (Cont.)
The 5 IP classes are split up based on the value in the 1st octet:

## Slide 7: IP Address Classes (Cont.)
Using the ranges, you can determine the class of an address from its 1st octet value.
An address beginning with 120 is a Class A address, 155 is a Class B address & 220 is a Class C address.

## Slide 8: Are You the Host or the Network?
The 32 bits of the IP address are divided into Network & Host portions, with the octets assigned as a part of one or the other.
Network & Host Representation
By IP Address Class
Class
Octet1
Octet2
Octet3
Octet4
Class A
Network
Host
Host
Host
Class B
Network
Network
Host
Host
Class C
Network
Network
Network
Host

## Slide 9: Are You the Host or the Network? (Cont.)
Each Network is assigned a network address & every device or interface (such as a router port) on the network is assigned a host address.
There are only 2 specific rules that govern the value of the address.

## Slide 10: Are You the Host or the Network? (Cont.)
A host address cannot be designated by all zeros or all ones.
These are special addresses that are reserved for special purposes.

## Slide 11: Class A Addresses
Class A IP addresses use the 1st 8 bits (1st Octet) to designate the Network address.
The 1st bit which is always a 0, is used to indicate the address as a Class A address & the remaining 7 bits are used to designate the Network.
The other 3 octets contain the Host address.

## Slide 12: Class A Addresses (Cont.)
There are 128 Class A Network Addresses, but because addresses with all zeros aren’t used & address 127 is a special purpose address, 126 Class A Networks are available.

## Slide 13: Class A Addresses (Cont.)
There are 16,777,214 Host addresses available in a Class A address.
Rather than remembering this number exactly, you can use the following formula to compute the number of hosts available in any of the class addresses, where “n” represents the number of bits in the host portion:
(2n – 2) = Number of available hosts

## Slide 14: Class A Addresses (Cont.)
For a Class A network, there are:
224 – 2 or 16,777,214 hosts.
Half of all IP addresses are Class A addresses.
You can use the same formula to determine the number of Networks in an address class.
Eg., a Class A address uses 7 bits to designate the network, so (27 – 2) = 126 or there can be 126 Class A Networks.

## Slide 15: Class B IP Addresses
Class B addresses use the 1st 16 bits (two octets) for the Network address.
The last 2 octets are used for the Host address.
The 1st 2 bit, which are always 10, designate the address as a Class B address & 14 bits are used to designate the Network. This leaves 16 bits (two octets) to designate the Hosts.

## Slide 16: Class B IP Addresses (Cont.)
So how many Class B Networks can there be?
Using our formula, (214 – 2), there can be 16,382 Class B Networks & each Network can have (216 – 2) Hosts, or 65,534 Hosts.

## Slide 17: Class C IP Addresses
Class C addresses use the 1st 24 bits (three octets) for the Network address & only the last octet for Host addresses.the 1st 3 bits of all class C addresses are set to 110, leaving 21 bits for the Network address, which means there can be 2,097,150 (221 – 2) Class C Networks, but only 254 (28 – 2) Hosts per Network.

## Slide 18: Class C IP Addresses (Cont.)

## Slide 19: Special Addresses
A few addresses are set aside for specific purposes.
Network addresses that are all binary zeros, all binary ones & Network addresses beginning with 127 are special Network addresses.

## Slide 20: Special Addresses (Cont.)

## Slide 21: Special Addresses (Cont.)
Within each address class is a set of addresses that are set aside for use in local networks sitting behind a firewall or NAT (Network Address Translation) device or Networks not connected to the Internet.

## Slide 22: Special Addresses (Cont.)
A list of these addresses for each IP address class:

## Slide 23
Credit:
peter.joseph.smith@tafensw.edu.au